## Slide 1
design:
use:
build:
ubicomp lab
university of washington
sustainability research
university of washington
A Longitudinal Study of Pressure Sensing to Infer Real-World Water Usage Events in the Home
Eric Larson, Jon Froehlich, Elliot Saba, Tim Campbell, Les Atlas, James Fogarty and Shwetak Patel
Notes: good morning, My name is Eric Larson and I am an EE student at the University of Washington in the laboratory of Ubiquitous computing. Today I want to talk with you about work in water usage sensing – this is a largely collaborative project lead by Jon Froehlich and myself.

## Slide 2
kitchen sink
28 gallons
refrigerator 0.3 gallons
dishwasher
6.5 gallons
today‘s usage
Notes: imagine a system that could tell you exactly how much water you have used in the kitchen today.

## Slide 3
toilet
78.4 gallons
shower 62.4 gallons
bath
6.5 gallons
bathroom sink 1 4.2 gallons
bathroom sink 2 0.8 gallons
today‘s usage
Notes: or from each fixture in the bathroom.
And that this system could also tell you the amount of hot and cold water usage from each fixture.

## Slide 4
toilet
78.4 gallons
shower 10.4 gallons
bath
0.0 gallons
bathroom sink 1 1.2 gallons
bathroom sink 2 0.8 gallons
shower 52.4 gallons
bath
6.5 gallons
bathroom sink 1 3.2 gallons
bathroom sink 2 2.4 gallons
today‘s usage: hot vs. cold
Notes: or from each fixture in the bathroom.
And that this system could also tell you the amount of hot and cold water usage from each fixture.

## Slide 5
sustainability applications
Notes: such a system has a number of applications in spaces like sustainability for eco feedback monitoring.

## Slide 6
assisted living applications
last active:
10:03PM
last active:
10:08PM
last active:
7:20AM
last active:
10:09PM
last active:
10:33PM
Notes: and in activity inference applications. Where such a system might be used for elder care, alerting you on your phone if it sees that your grandma edith isnt following her normal morning routine.

## Slide 7
water resource management

## Slide 8
at ubicomp09, we introduced hydrosense
Notes: towards this vision, we presented work in 2009 on a system called hydrosense.

## Slide 9
single, screw-on sensor
identifies fixture usage
estimates flow
hydrosense
Froehlich et al., UbiComp2009; Larson et al., PMC2010
Notes: hydrosense is a single screw on sensor
that identifies water usage down to the fixture level
and provides estimates of water flow from each fixture

## Slide 10
hydrosense
uses pressure waves to identify usage
bath open
dishwasher open
upstairs toilet flush
downstairs toilet flush
downstairs shower open
kitchen sink
cold open
kitchen sink
hot open
kitchen sink
hot open
Notes: the key insight behind hydrosense is that when you open or close a water fixture in your home it generates a pressure wave inside the entire plumbing system and these pressure waves look unique for each fixture,
furthermore, fixtures of the same type, but located at different points in the home also have unique pressure transients (here I am showing two toilet signatures)
and even the hot and cold water valves inside the same fixture look different from one another

## Slide 11
controlled experiments
2 researchers per site
5 trials per valve
experimental script
valve opened full stop
pause for ~5 seconds
valve closed
ubicomp2009 feasibility study
Notes: in our previous work we conducted a feasibility studyshowing these pressure waves were unique

## Slide 12
ubicomp2009 data collection
Notes: and we did this using controlled experiments where a group of researchers came into a home and staged experiments for each valve in the home.
As you can see, one experimenter activated the water, and the other labeled the pressure stream in real time.

## Slide 13
Chart: 
| H1 (12 valves) | H2 (8 valves) | H3 (6 valves) | H4 (5 valves) | H5 (9 valves) | H6 (8 valves) | H7 (8 valves) | H8 (6 valves) | H9 (7 valves) | H10 (7 valves) | Aggregate | Overall
Open Events | 1 | 0.964 | 1 | 0.962 | 1 | 1 | 1 | 1 | 0.971 | 0.971 | 0.989 | 0.979
Close Events | 1 | 1 | 1 | 1 | 1 | 0.9 | 1 | 0.971 | 0.971 | 0.771 | 0.968
fixture classification results
by home
10-fold cross validation
Notes: This figure shows the accuracy of fixture-level identification of valve open and valve close events within each home as well as the aggregate 97.9% accuracy of fixture-level classification.
Many homes resulted in 100% open and close fixture classification.
The worst performing house, H10, was due to noise from the eleven cabins that share the same supply line at the resort.

## Slide 14
successfully demonstrated the potential of using pressure waves to identify fixture usage
ubicomp2009 paper
evaluation method
staged experiments
all faucet handles were operated at approximately the same flow rates
all fixtures were tested in isolation
algorithm
each pressure wave treated independently
did not consider context of usage
was not probabilistic
Notes: while this showed the potential for using pressure waves for fixture usage classification, it had a number of drawbacks
the evaluation was staged so faucets were not operated at a variety of different flow rates and all fixtures were tested in isolation
furthermore our algorithm looked at pressure waves independently without considering the context in which they were used

## Slide 15
what we’re really interested in…
how well will hydrosense perform on real-world water usage data?

## Slide 16
brushing teeth

## Slide 17
shaving

## Slide 18
bathing

## Slide 19
paw washing

## Slide 20
water tower
water tower
thermal
expansion
tank
hose
spigot
utility water meter
pressure regulator
laundry
bathroom 1
hot
water heater
bathroom 2
dishwasher
incoming cold water from supply line
kitchen
compound events
Notes: or when doing all of these activities at the same time

## Slide 21
pervasive 2011 contributions
longitudinal study of real-world water usage and the resulting dataset
a new probabilistic approach to water usage classification
demonstrate that this new approach can accurately classify real world data
1
2
3
Notes: today I am going to talk about how we evaluated hydrosense in a longitudinal study
the algorithms we developed
and show how accurate the results were

## Slide 22
ground truth sensors
5-week deployment
classification algorithm
classification results
Notes: I will first discuss the sensors we used to collect labeled water usage data, then discuss our five week deployment of the technology, the algorithms, and how well we did.

## Slide 23
ground truth sensors
5-week deployment
classification algorithm
classification results
Notes: we’ll start with the ground truth sensors

## Slide 24
ground truth labels
manual
kitchen sink
cold
open
cold
close
kitchen sink
hot
open
hot
close
bathroom sink
cold
open
cold
close
automatic
Notes: obviously the manual annotation we used in previous work won’t scale to a longitudinal study – we couldn’t have an undergrad with a laptop in your bathroom labeling water usage as you took a shower – although maybe that would have been easier.
We need a way of automating that labeling process.

## Slide 25
water tower
thermal
expansion
tank
hose
spigot
utility water meter
pressure regulator
laundry
bathroom 1
hot
water heater
bathroom 2
dishwasher
incoming cold water from supply line
kitchen
Notes: so in addition installing the hydrosense system, we need to install a wireless network of sensors at every fixture that uses water in the home so we can label the water usage we see from the hydrosense system.

## Slide 26
how can we obtain water usage labels at the valve-level?
Notes: and the real question is how we install this wireless network so that we can sense water usage down to the valve level – that is so that the sensors tell us the temperature state of the fixture.

## Slide 27
this is actually a challenging question…

## Slide 28
kitchen sink
bathroom sink
toilet
bath
shower
laundry basin
washing machine
dishwasher
function across fixtures
Notes: there is an incredible amount of diversity in the water fixtures in our homes – even just looking at sinks, there are diverse ways of activating flow, and we also need a way of looking at appliances like the clothes and dish washers.

## Slide 29
after many failed attempts

## Slide 30
reed switch
3-axis accelerometer
hall
effect
unidirectional ball switch
omnidirectional ball switch
xbee wireless modem
fixture usage sensor board
custom ground truth data collection system
Notes: we ended up with these sensors. there is the wireless transmitter and custom base, which connects

## Slide 31
reed switch
3-axis accelerometer
hall
effect
unidirectional ball switch
omnidirectional ball switch
xbee wireless modem
fixture usage sensor board
custom ground truth data collection system
“wake up” sensors
Notes: to a wake up sensor, which wakes the modem and tells it to sample data.

## Slide 32
reed switch
3-axis accelerometer
hall
effect
unidirectional ball switch
omnidirectional ball switch
xbee wireless modem
fixture usage sensor board
custom ground truth data collection system
fixture handle
position sensors
Notes: from one of three fixture position sensors. We used magnets attached to the faucets and either reed switches or hall effect sensors to know when a valve was opened or closed, or an accelerometer.

## Slide 33
accelerometer
Notes: for example, we attached an accelerometer to a single handle sink in order to get the handle position (and thus the temperature and flow state).

## Slide 34
reed switch
3-axis accelerometer
hall
effect
unidirectional ball switch
omnidirectional ball switch
xbee wireless modem
fixture usage sensor board
custom ground truth data collection system
push button
xbee wireless transmitter
fixture usage sensor board
thermistor
modified kill-a-watt
Notes: for appliances we used a modified KAW sensor to know when the appliance was drawing power.

## Slide 35
ground truth sensors
5-week deployment
classification algorithm
classification results
Notes: and now it was a matter of installing this ground truth sensor network and the hydrosense system in real homes

## Slide 36
residents | 2 | 2 | 4 | 2 | 2
size | 3000 sqft | 750 sqft | 1200 sqft | 700 sqft | 750 sqft
floors | 3 | 2 | 2 | 3rd flr | 6th flr
fixtures | 17 | 8 | 13 | 8 | 8
valves | 28 | 13 | 21 | 13 | 13
deployment sites
Notes: we chose three homes and two apartments of varying sizes and residents. And in all we almost 90 different water valves

## Slide 37
deployment infrastructure
ground truth sensor on every valve
pressure sensor
a laptop running hydrologger
xbee
bluetooth
http
backend python hydroserver
Notes: each deployment site had ground truth and hydrosense sensors communicating to a laptop which logged all the data. The laptop uploaded the data to a webserver, which backed up the data and also alerted us by email if a sensor was malfunctioning or if there was a problem with the logger.

## Slide 38
pressure sensor 1
(hot point)
pressure sensor 2
(cold point)
home 1
apartment 1
two pressure sensors per home
pressure sensor 2
(hot point)
pressure sensor 1
(cold point)
Notes: additionally we installed two sensors at each deployment site in order to experiment with using more than one sensor. One was on the cold water line and the other on the hot water line. Shown here for a house and one of the apartments.

## Slide 39
Notes: and in the end the deployment sites looked like this, here is a subset of the sinks we instrumented

## Slide 40
Notes: toilets

## Slide 41
Notes: and showers. Notice that we also had to instrument the diverter valve to know whether the bath or shower was running, in addition to secondary shower handles.

## Slide 42
Notes: here is a clothes washer. We also tied a thermistor on the drain valve of the washer in order to know whether the homeowner used a hot/cold or cold/cold cycle.

## Slide 43
Notes: and even instrumenting things like the refidgerator water dispenser.

## Slide 44
pressure stream
red = hot line
blue = cold line
reed switches
high = active
low = inactive
Notes: (maybe skip)
so at any given deployment site you might see a logger like this with pressure streams shown and the values from our reed switch sensors

## Slide 45
Notes: as you can see the toilet is activated, and we see a reed switch change states, and then when the hot water is used, we see more sensors change state
all of this data gets logged

## Slide 46
hydrosense annotations
2. semi-automated label
3. review annotator
4. verification
5. final label
1. ground truth sensor
Notes: and now we need to make sense of the ground truth data in order to get labels
so the process is designed to get the most accurate data possible: a user accesses the ground truth data stream, semi-autmaitcally generates labels, then review those labels, after wards a different annotator reviews those labels, checking for mistakes until we have a final label that we can absolutely trust.

## Slide 47
toilet closing
That
Ground truth
ground truth labeling
Notes: A Hall effect sensor is a transducer that varies its output voltage in response to changes in magnetic field.
A reed switch is an electrical switch operated by an applied magnetic field

## Slide 48
dual pressure sensor
toilet
bathroom faucet
kitchen faucet
dishwasher
washing machine
bath/shower
bath/shower diverter
Notes: . We built a custom tool that shows the pressure streams.
and every sensor in the residence.

## Slide 49
dual pressure sensor
toilet
bathroom faucet
kitchen faucet
dishwasher
washing machine
bath/shower
bath/shower diverter

## Slide 50
toilet
bathroom faucet
kitchen faucet
dishwasher
washing machine
bath/shower
bath/shower diverter
dual pressure sensor
Notes: where a user highlights where activity occurs and has the tool and semi-automatically generates where it thinks the pressure stream should be annotated.

## Slide 51
Notes: here we see a more complicated example. Where the user uses auto generate and then must go through each label and make sure it is correct.

## Slide 52
hydrosense annotations
2. semi-automated label
3. review annotator
4. verification
5. final label
1. ground truth sensor
Notes: so the process is designed to get the most accurate data possible: a user accesses the ground truth data stream, semi-autmaitcally generates labels, then review those labels, after wards a different annotator reviews those labels, checking for mistakes until we have a final label that we can absolutely trust.

## Slide 53
 |  |  |  |  |  | totals
days | 33 | 33 | 30 | 27 | 33 | 156
events | 2374 | 3075 | 4754 | 2499 | 2578 | 14,960
events/day | 71.9 | 93.2 | 158.5 | 92.6 | 78.1 | 95.9
compound | 22.2% | 21.8% | 16.6% | 32% | 21.3% | 21.9%
5-week dataset
22% of all events were compound
Notes: and at the end of the labeling process we ended up with 156 days of water use spread out among 5 deployment sites and almost 15000 water usage labels to evaluate our hydrosense system. One thing that was quite surpirsing was that 22% off all the pressure waves we collected were compound events, that is, more than one water source was on at the same time.

## Slide 54
ground truth sensors
5-week deployment
classification algorithm
classification results
Notes: so now let’s talk about how we used this dataset to build a probabilistic algorithm

## Slide 55
toilet
natural water use
70
50
30
pressure (psi)
kitchen sink
kitchen sink
bathroom sink
Notes: so a common pressure stream might look something like this. Which of course is wildly different than anything we did with staged experiments. We saw a tremendous amount of variability in the pressure waves.. So we decided to focus on how classifiable these pressure waves were.
That is we use the segmentation from our hand annotations and developed an algorithm to classify the pressure waves in our database, leaving segmentation for future work. Honestly, if the pressure waves aren’t classifiable, there is no need to develop a segmentation algorithm.

## Slide 56
signal
behavior
bayesian inference
Notes: So we really had to go back to the drawing board and rethink our algorithmic approach from previous work. This giant equation is just a multiplication of a large number of probability scores.
Our new algorithm borrows from Bayesian inference in speech recognition, instead of classifying vocal utterances as words, we classify pressure transients as openings and closings. And just like in speech recognition, which may use a grammar and a language model to help with classification, so do we. The grammar and language model enables us to look at additional features, which we call paired valve priors. I’ll go over each in turn.
The first term here deals primarily with signal level characteristics, and the last three terms deal mostly with leveraging human behavior around water usage. We will start with the first term.

## Slide 57
toilet
unclassified event
term(i) template matching
compare across multiple signal transformations
dishwasher
kitchen faucet
shower
event library
Notes: the first term uses a template matching approach, where we compare an unknown event to events that we have saved in a library.

## Slide 58
unclassified event
event library
toilet
unclassified event
dishwasher
kitchen faucet
detrendedshower
derivativeshower
cepstrumshower
shower
signal transforms
Notes: in particular we make use of signal transformations And we compare the percent correlation between each transformation of the unknown event and the library of events. We use 8 transformations in all, but I will briefly mention four here.

## Slide 59
toilet
dishwasher
kitchen faucet
shower
unclassified event
event library
unclassified event
assess similarity
15%
55%
18%
9%
signal transforms
Notes: in particular we make use of signal transformations And we compare the percent correlation between each transformation of the unknown event and the library of events. We use 8 transformations in all, but I will briefly mention four here.

## Slide 60
hydrosense
example pressure waves
bath open
dishwasher open
upstairs toilet flush
downstairs toilet flush
downstairs shower open
kitchen sink
cold open
kitchen sink
hot open
kitchen sink
hot open
Notes: To motivate these transformations, we need to return to the plumbing system. When we activate a fixture in the plumbing system, the entire system responds instantaneously, like letting the air out of a balloon. Depending on where we activate the water in the system, different resonances will be excited – so it will be important which resonances are activated and, as you can see from these examples, how quickly those resonances die out over time.

## Slide 61
unclassified event
event library
toilet
unclassified event
dishwasher
kitchen faucet
shower
signal transforms

## Slide 62
Chart: 
Chart: 
Chart: 
derivative
(psi/s)
time (s)
Chart: 
Chart: 
smoothed pressure
(psi)
Chart: 
Chart: 
raw pressure (psi)
term(i): filter transforms
detrended
derivative
term(i) template matching
filter transforms
signal transforms
Notes: so the signal transformations we chose are designed to highlight the fall off of different resonances.
the first template we save is the raw waveform, detrended.
next we calculate the derivative of the low frequency resonance using a low pass filter followed by a derivative operation.
we save this template which highlights the falloff of the low frequency resonance

## Slide 63
Chart: 
Chart: 
bandpass
derivative
(psi/s)
time (s)
Chart: 
smoothed pressure
(psi)
Chart: 
raw pressure (psi)
Chart: 
detrended
derivative
bandpass derivative
term(i) template matching
filter transforms
signal transforms
Notes: but also notice that there is a high frequency resonance in this wave.
We can isolate that by subtracting the low pass filtered wave from the raw waveform and then taking the derivative. We save this template which isolates the falloff of the second resonance.

## Slide 64
frequency
Chart: 
raw pressure (psi)
detrended
derivative
bandpass derivative
Chart: 
cepstral
amplitude
index
cepstrum
term(i) template matching
filter transforms
signal transforms
Notes: lastly we employ a frequency based transform called the cepstrum, which uses a set of filter banks and a log operation. The values of the cepstrum are largely influenced by where water is activated in the plumbing system, so we can expect it to stay more or less constant regardless of the flow rate at which the fixture is activated.

## Slide 65
unclassified event
event library
toilet
unclassified event
dishwasher
kitchen faucet
shower
detrended
derivative
bandpass derivative
cepstrum
signal transforms
Notes: so we compare theses signal transforms of the unknown wave to saved transformations in our library. In this example, if we want to know the probability that the kitchen sink was the origin of this unknown wave, we can multiply all the transformations together to get a single probability.

## Slide 66
unclassified event
event library
toilet
unclassified event
dishwasher
kitchen faucet
detrended
derivative
bandpass derivative
cepstrum
55%
85%
65%
90%
detrended
derivative
bandpass derivative
cepstrum
signal transforms
Notes: so we compare theses signal transforms of the unknown wave to saved transformations in our library. In this example, if we want to know the probability that the kitchen sink was the origin of this unknown wave, we can multiply all the transformations together to get a single probability.

## Slide 67
signal transforms
unclassified event
event library
toilet
unclassified event
dishwasher
kitchen faucet
detrended
derivative
bandpass derivative
cepstrum
55%
85%
65%
90%
detrended
derivative
bandpass derivative
cepstrum
template comparisons
Notes: which makes up a portion of term I the other portion of term 1 is made from features of the signal, not templates.

## Slide 68
bath
toilet
unclassified event
term(i) signal features
shower
event library
Notes: which makes up a portion of term I the other portion of term 1 is made from features of the signal, not templates.

## Slide 69
unclassified event
term(i) signal features
shower
toilet
bath
toilet
pressure drop
Notes: the other portion of term 1 is made from features of the signal, not templates.
the first feature we compare is the pressure drop of the event shown here for different events n the library. Pressure drop is basically an uncalibrated measure of flow rate. Since different valves have different flow rates, we can compare the unknown valve’s pressure drop to those we have in our database.

## Slide 70
term(i) signal features
shower
toilet
bath
toilet
resonance tracking
unclassified event
Notes: In the same way, we can explicitly model the frequency and magnitude of the excited resonances in the pressure wave and compare them across the library of events. We chose an autoregressive model, but others are possible.

## Slide 71
term(i) signal features
shower
toilet
bath
toilet
resonance tracking
unclassified event
signal feature comparisons
template comparisons
Notes: Finally, we can then combine the signal features and template features by multiplication to form term (i)

## Slide 72
70
50
30
pressure
P(kitchen sink hot open)
14%
P(kitchen sink cold open)
P(toilet open)
P(kitchen hot/cold close)
P(kitchen hot close)
P(toilet close)
3%
15%
2%
6%
1%
term (i): templates and signal features
Notes: so an unknown pressure transient comes along, we can use term one to find the probability that the originator of this valve was the kitchen sink hot valve opening. We just combine all the signal features we have from the kitchen sink. And we can do this for every example valve in our library.

## Slide 73
70
50
30
pressure
P(kitchen sink hot open)
14%
P(kitchen sink cold open)
P(toilet open)
P(kitchen hot/cold close)
P(kitchen hot close)
P(toilet close)
3%
15%
2%
6%
1%
term (i): templates and signal features
Notes: and if you wanted to you could stop here and use the likeliest pressure wave – and our ubicomp 2009 work did just that except using a subset of the features I have described here.

## Slide 74
70
50
30
pressure
P(kitchen sink hot open)
14%
P(kitchen sink cold open)
P(toilet open)
P(kitchen hot/cold close)
P(kitchen hot close)
P(toilet close)
3%
15%
2%
6%
1%
term (ii): bigram language model
Notes: or we can be a little smarter when more than one pressure wave is present, and incorporate our second term, a language model, with the first term. so we first build a trellis of all the fixture probabilities using term 1. (shown here as blue dots)
But then we use the language model to combine the terms using transition probabilities. That is, we know the probability of the each pressure wave going to the next.
I will show a subset of those transition probabilities here. So we navigate the trellis using these transition probabilities.

## Slide 75
70
50
30
pressure
P(kitchen sink hot open)
14%
P(kitchen sink cold open)
P(toilet open)
P(kitchen hot/cold close)
P(kitchen hot close)
P(toilet close)
3%
15%
2%
6%
1%
term (ii): bigram language model
Notes: or we can be a little smarter when more than one pressure wave is present, and incorporate our second term, a language model, with the first term. so we first build a trellis of all the fixture probabilities using term 1. (shown here as blue dots)
But then we use the language model to combine the terms using transition probabilities. That is, we know the probability of the each pressure wave going to the next.
I will show a subset of those transition probabilities here. So we navigate the trellis using these transition probabilities.

## Slide 76
70
50
30
pressure
P(kitchen sink hot open)
14%
P(kitchen sink cold open)
P(toilet open)
P(kitchen hot/cold close)
P(kitchen hot close)
P(toilet close)
3%
15%
2%
6%
1%
Toilet | Faucet | Dishwasher | Shower | Bath | Washer | 
0.10 | 0.08 | 0.12 | 0.09 | 0.08 | 0.03 | Toilet
0.13 | 0.42 | 0.09 | 0.54 | 0.31 | 0.03 | Faucet
0.01 | 0.01 | 0.34 | 0.01 | 0.01 | 0.01 | Dishwasher
0.01 | 0.01 | 0.01 | 0.01 | 0.15 | 0.01 | Shower
0.04 | 0.03 | 0.01 | 0.01 | 0.25 | 0.01 | Bath
0.01 | 0.01 | 0.01 | 0.02 | 0.01 | 0.66 | Washer
term (ii): bigram language model
Notes: or we can be a little smarter when more than one pressure wave is present, and incorporate our second term, a language model, with the first term. so we first build a trellis of all the fixture probabilities using term 1. (shown here as blue dots)
But then we use the language model to combine the terms using transition probabilities. That is, we know the probability of the each pressure wave going to the next.
I will show a subset of those transition probabilities here. So we navigate the trellis using these transition probabilities.

## Slide 77
70
50
30
pressure
P(kitchen sink hot open)
14%
P(kitchen sink cold open)
P(toilet open)
P(kitchen hot/cold close)
P(kitchen hot close)
P(toilet close)
3%
15%
2%
6%
1%
term (ii): bigram language model
Toilet | Faucet | Dishwasher | Shower | Bath | Washer | 
0.10 | 0.08 | 0.12 | 0.09 | 0.08 | 0.03 | Toilet
0.13 | 0.42 | 0.09 | 0.54 | 0.31 | 0.03 | Faucet
0.01 | 0.01 | 0.34 | 0.01 | 0.01 | 0.01 | Dishwasher
0.01 | 0.01 | 0.01 | 0.01 | 0.15 | 0.01 | Shower
0.04 | 0.03 | 0.01 | 0.01 | 0.25 | 0.01 | Bath
0.01 | 0.01 | 0.01 | 0.02 | 0.01 | 0.66 | Washer
Notes: and we can choose the most likely “sequence” of pressure waves, not just the most likely pressure wave. And if we wanted we could stop there.

## Slide 78
70
50
30
pressure
P(kitchen sink hot open)
14%
P(kitchen sink cold open)
P(toilet open)
P(kitchen hot/cold close)
P(kitchen hot close)
P(toilet close)
3%
15%
2%
6%
1%
term (ii): bigram language model
Toilet | Faucet | Dishwasher | Shower | Bath | Washer | 
0.10 | 0.08 | 0.12 | 0.09 | 0.08 | 0.03 | Toilet
0.13 | 0.42 | 0.09 | 0.54 | 0.31 | 0.03 | Faucet
0.01 | 0.01 | 0.34 | 0.01 | 0.01 | 0.01 | Dishwasher
0.01 | 0.01 | 0.01 | 0.01 | 0.15 | 0.01 | Shower
0.04 | 0.03 | 0.01 | 0.01 | 0.25 | 0.01 | Bath
0.01 | 0.01 | 0.01 | 0.02 | 0.01 | 0.66 | Washer
Notes: Or we could find the likelihood of the N best sequences through the trellis.
Shown here for the entire sequence. Maybe the best probabilities are 4.6, 4.3 , and 4.1 % likelihood.
But the trellis view makes it harder to see the n best paths, so instead let’s list out each sequence.

## Slide 79
70
50
30
pressure
P(kitchen sink hot open)
14%
P(kitchen sink cold open)
P(toilet open)
P(kitchen hot/cold close)
P(kitchen hot close)
P(toilet close)
3%
15%
2%
6%
1%
term (ii): bigram language model
Notes: Or we could find the likelihood of the N best sequences through the trellis.
Shown here for the entire sequence. Maybe the best probabilities are 4.6, 4.3 , and 4.1 % likelihood.
But the trellis view makes it harder to see the n best paths, so instead let’s list out each sequence.

## Slide 80
70
50
30
pressure
P(kitchen sink hot open)
14%
P(kitchen sink cold open)
P(toilet open)
P(kitchen hot/cold close)
P(kitchen hot close)
P(toilet close)
3%
15%
2%
6%
1%
4.6%
4.3%
4.1%
term (ii): bigram language model
sequence 1
sequence 2
sequence 3
Notes: Or we could find the likelihood of the N best sequences through the trellis.
Shown here for the entire sequence. Maybe the best probabilities are 4.6, 4.3 , and 4.1 % likelihood.
But the trellis view makes it harder to see the n best paths, so instead let’s list out each sequence.

## Slide 81
70
50
30
pressure
kitchen sink
hot open
kitchen sink
cold open
dishwasher
open
bathroom sink
hot close
kitchen sink
hot close
toilet
open
toilet
close
kitchen sink
hot close
kitchen sink
hot open
shower
cold open
toilet
open
bathroom sink
hot close
kitchen sink
hot close
kitchen sink
hot open
kitchen sink
hot close
kitchen sink
hot close
kitchen sink
hot open
toilet
open
bathroom sink
hot open
bathroom sink
hot close
kitchen sink
hot close
kitchen sink
hot open
kitchen sink
hot close
toilet
close
sequence 1
sequence 2
sequence 3
term (ii): bigram language model
Notes: Now we can add our third term, since we have a language for valve usage, we can also have a grammar. Similar to the grammar in speech recognition, there is a grammar for the way pressure waves should be combined.

## Slide 82
term(iii): grammar
opened closed
opened closed
temperature consistency
1
2
3
soft penalty
Notes: the grammar we created is simple:
if we come across a fixture open event in the sequence, like a kitchen sink, we should see a kitchen sink close later on the sequence.
if we come across a fixture close event, we should have already seen an open event in the sequence.
and lastly the open and close should have consistent temperatures, so if the hot valve is opened in the kitchen, it should be closed by a hot valve.
we apply this grammar with a soft penalty -> we do not eliminate sequences that contain impossible valve impairings, instead we impose a penalty on those sequences for each grammatical mistake.

## Slide 83
70
50
30
pressure
kitchen sink
hot open
kitchen sink
cold open
dishwasher
open
bathroom sink
hot close
kitchen sink
hot close
toilet
open
toilet
close
kitchen sink
hot close
bathroom sink
hot open
shower
cold open
toilet
open
bathroom sink
hot close
shower
cold close
kitchen sink
hot open
toilet
close
kitchen sink
hot close
kitchen sink
hot open
toilet
open
bathroom sink
hot open
bathroom sink
hot close
kitchen sink
hot close
kitchen sink
hot open
kitchen sink
hot close
toilet
close
term(iii): grammar
sequence 1
sequence 2
sequence 3
Notes: so we identify errors in the sequences, apply a penalty to the probability of the sequence and reorder the sequences.
based on their new probabilities.
now everything that was not penalized by the grammar can be paired together. So the bathroom sink can be paired the shower, and son on. This is a vital piece of knowledge that allows us to incorporate our last term which we call paired valve priors.

## Slide 84
70
50
30
pressure
bathroom sink
hot open
shower
cold open
toilet
open
bathroom sink
hot close
shower
cold close
kitchen sink
hot open
toilet
close
kitchen sink
hot close
kitchen sink
hot open
toilet
open
bathroom sink
hot open
bathroom sink
hot close
kitchen sink
hot close
kitchen sink
hot open
kitchen sink
hot close
toilet
close
term(iii): grammar
kitchen sink
hot open
kitchen sink
cold open
dishwasher
open
bathroom sink
hot close
kitchen sink
hot close
toilet
open
toilet
close
kitchen sink
hot close
Notes: so we identify errors in the sequences, apply a penalty to the probability of the sequence and reorder the sequences.
based on their new probabilities.
now everything that was not penalized by the grammar can be paired together. So the bathroom sink can be paired the shower, and son on. This is a vital piece of knowledge that allows us to incorporate our last term which we call paired valve priors.

## Slide 85
70
50
30
pressure
bathroom sink
hot open
shower
cold open
toilet
open
bathroom sink
hot close
shower
cold close
kitchen sink
hot open
toilet
close
kitchen sink
hot close
kitchen sink
hot open
toilet
open
bathroom sink
hot open
bathroom sink
hot close
kitchen sink
hot close
kitchen sink
hot open
kitchen sink
hot close
toilet
close
term(iii): grammar
kitchen sink
hot open
kitchen sink
cold open
dishwasher
open
bathroom sink
hot close
kitchen sink
hot close
toilet
open
toilet
close
kitchen sink
hot close
Notes: so we identify errors in the sequences, apply a penalty to the probability of the sequence and reorder the sequences.
based on their new probabilities.
now everything that was not penalized by the grammar can be paired together. So the bathroom sink can be paired the shower, and son on. This is a vital piece of knowledge that allows us to incorporate our last term which we call paired valve priors.

## Slide 86
70
50
30
pressure
bathroom sink
hot open
shower
cold open
toilet
open
bathroom sink
hot close
shower
cold close
kitchen sink
hot open
toilet
close
kitchen sink
hot close
kitchen sink
hot open
toilet
open
bathroom sink
hot open
bathroom sink
hot close
kitchen sink
hot close
kitchen sink
hot open
kitchen sink
hot close
toilet
close
term(iii): grammar
kitchen sink
hot open
kitchen sink
cold open
dishwasher
open
bathroom sink
hot close
kitchen sink
hot close
toilet
open
toilet
close
kitchen sink
hot close
Notes: so we identify errors in the sequences, apply a penalty to the probability of the sequence and reorder the sequences.
based on their new probabilities.
now everything that was not penalized by the grammar can be paired together. So the bathroom sink can be paired the shower, and son on. This is a vital piece of knowledge that allows us to incorporate our last term which we call paired valve priors.

## Slide 87
fixture usage duration
flow volume
term(iv): paired valve priors
Chart: 
estimated flow volume
30
150
60
90
120
seconds
bin frequency
3
9
6
estimated gallons
1
12
open
close
faucet
toilet
bath
faucet
toilet
bath
paired
Notes: so we no longer need to think just about pressure waves, but instead, because waves are paired together, we can think about fixture usage. .
for example, duration of use. If we look at histograms for the duration of a faucet use, its different than a toilet which is different than a bath.
in the same way estimated volume of water used should be different for each fixture. Pairing pressure waves allows us to incorporate these probabilities

## Slide 89
70
50
30
pressure
term(iv): paired valve priors
kitchen sink
hot open
kitchen sink
cold open
dishwasher
open
bathroom sink
hot close
kitchen sink
hot close
toilet
open
toilet
close
kitchen sink
hot close
kitchen sink
hot open
toilet
open
bathroom sink
hot open
bathroom sink
hot close
kitchen sink
hot close
kitchen sink
hot open
kitchen sink
hot close
toilet
close
bathroom sink
hot open
shower
cold open
toilet
open
bathroom sink
hot close
shower
cold close
kitchen sink
hot open
toilet
close
kitchen sink
hot close
Notes: and reorder the list for each paired event.
and finally choose the most likely event from the list.

## Slide 90
70
50
30
pressure
kitchen sink
hot open
kitchen sink
cold open
dishwasher
open
bathroom sink
hot close
kitchen sink
hot close
toilet
open
toilet
close
kitchen sink
hot close
kitchen sink
hot open
toilet
open
bathroom sink
hot open
bathroom sink
hot close
kitchen sink
hot close
kitchen sink
hot open
kitchen sink
hot close
toilet
close
bathroom sink
hot open
shower
cold open
toilet
open
bathroom sink
hot close
shower
cold close
kitchen sink
hot open
toilet
close
kitchen sink
hot close
term(iv): paired valve priors
Notes: and reorder the list for each paired event.
and finally choose the most likely event from the list.

## Slide 91
70
50
30
pressure
kitchen sink
hot open
toilet
open
bathroom sink
hot open
bathroom sink
hot close
kitchen sink
hot close
kitchen sink
hot open
kitchen sink
hot close
toilet
close
term(iv): paired valve priors
toilet
kitchen sink
kitchen sink
bathroom sink
Notes: and reorder the list for each paired event.
and finally choose the most likely event from the list.
And we see that this is the example we saw from before.

## Slide 92
ground truth sensors
5-week deployment
classification algorithm
classification results
Notes: now let’s see how our algorithm performed.

## Slide 93
three levels of granularity
valve level
e.g., upstairs bathroom faucet hot water activated
1
fixture level
e.g., upstairs bathroom faucet activated
2
fixture category level
e.g., faucet activated
3
Notes: but we can break the results down by granularity of the sensing.
we can talk about results at the valve level, so knowing the exact bathroom sink hot valve that was activated.
or at the fixture level, so knowing that the bathroom faucet was activated, but we don’t care about the temperature state. If you do activity inference, this might be your main interest because it gives you location.
and finally we can talk about the fixture category level – so knowing only that a faucet was activated, but not where. For sustainability you might be interested in one or all of these levels of accuracy.

## Slide 94
Chart: 
 | 70.2017 | 72.4838 | 75.4914
 | 83.4264 | 87.9941 | 89.4856
 | 93.6134 | 95.3645 | 95.9173
hydrosense classification results
real-world water usage data
term (i)
fixture
valve
fixture category
Notes: so here are the results for using only term (i)

## Slide 95
Chart: 
 | 70.2017 | 72.4838 | 75.4914
 | 83.4264 | 87.9941 | 89.4856
 | 93.6134 | 95.3645 | 95.9173
70.2%
83.4%
93.6%
72.4%
88.0%
95.3%
75.5%
89.5%
95.9%
terms (i)-(iv)
term (i) + (ii)
hydrosense classification results
real-world water usage data
term (i)
*error bars = std error
fixture
valve
fixture category
*10-fold cross validation
Notes: 70% for the valve level, not bad. 83% at the fixture level, and 94% at the category level
if we add the language model, term ii, we get an increase in performance,
and using all terms we get the best performance increase. doing about 90% accurate at the fixture level, about 76 at the valve level.

## Slide 96
Chart: 
 | 70.2017 | 72.4838 | 75.4914
 | 83.4264 | 87.9941 | 89.4856
 | 93.6134 | 95.3645 | 95.9173
hydrosense classification results
real-world water usage data
terms (i)-(iv)
term (i) + (ii)
*error bars = std error
fixture
valve
fixture category
*10-fold cross validation
term (i)
70.2%
83.4%
93.6%
72.4%
88.0%
95.3%
75.5%
89.5%
95.9%
Notes: if we add the language model, term ii, we get an increase in performance,
and using all terms we get the best performance increase. doing about 90% accurate at the fixture level, about 76 at the valve level.

## Slide 97
Chart: 
 | 70.2017 | 72.4838 | 75.4914
 | 83.4264 | 87.9941 | 89.4856
 | 93.6134 | 95.3645 | 95.9173
Chart: 
| templ | templ+LM | templ+LM+priors
Isolated | 65.62 | 72.8 | 72.3
Compound | 80.84 | 87.16 | 86.22
category | 94.08 | 96.06 | 95.16
term (i)
*error bars = std error
terms (i)-(iv)
term (i) + (ii)
fixture
valve
fixture category
compound events
real-world water usage data
*10-fold cross validation
65.6%
80.8%
94.0%
72.8%
87.2%
96.0%
72.3%
86.2%
95.2%
Notes: now we can also look at the data in terms of compound events, which accounted for 22% of all the water activity in the deployment sites. I will leave up the overall results, but greyed out. Notice that term (i) results plummet,
but using term I and ii actually does the same on compound as it does overall (this makes sense because the language model makes us less reliant on the signal characteristics which change in a compound event).
But when we look at all the terms, we do get a drop in performance. This makes sense because the one feature we used, the estimated volume used, is dependent on the signal characteristics and is less reliable during a compound event. So while the last terms help overall, they actually hurt us during a compound event.
But now let’s probe the results space a little more and look only at the results when using all the terms.

## Slide 98
hydrosense classification results
real-world water usage data
Chart: 
 | 75.4914 | 89.4856 | 95.9173
 | 82.4176 | 93.4825 | 97.662
one sensor, terms(i)-(iv)
fixture category
fixture
valve
*error bars = std error
*10-fold cross validation
Notes: here are the results shown only for using all terms. Recall that we installed two pressure sensors

## Slide 99
Chart: 
 | 75.4914 | 89.4856 | 95.9173
 | 82.4176 | 93.4825 | 97.662
hydrosense classification results
real-world water usage data
two sensors, terms(i)-(iv)
fixture category
fixture
valve
*error bars = std error
*10-fold cross validation
*terms (i)-(iv)
one sensor, terms(i)-(iv)
Notes: The addition of a second sensor resulted in a marginal to medium (but significant) increase in classification accuracies across the board, surpassing 80% at the valve level all the way up to almost 98% at the category level.
But lastly let’s delve a little further into the 90% accuracy at the fixture level.

## Slide 100
…what about training?
Notes: and ask the question what about training?
10 fold cross validation assumes that we have a lot of data to use for classification. But how much calibration data do we really need?

## Slide 101
Chart: Days of Training Data
| 1 | 3 | 5 | 7 | 10
pipes | 68.9353 | 78.8351 | 80.5773 | 82.352 | 82.9633
hydrosense training results
real-world water usage data
term (i)
*error bars = std error

## Slide 102
Chart: Days of Training Data
| 1 | 3 | 5 | 7 | 10
pipes | 68.9353 | 78.8351 | 80.5773 | 82.352 | 82.9633
pipes+LM | 76.503 | 86.3948 | 87.5797 | 88.3788 | 89.527
hydrosense training results
real-world water usage data
term (i)+(ii)
term(i)
*error bars = std error

## Slide 103
Chart: Days of Training Data
| 1 | 3 | 5 | 7 | 10
pipes | 68.9353 | 78.8351 | 80.5773 | 82.352 | 82.9633
pipes+LM | 76.503 | 86.3948 | 87.5797 | 88.3788 | 89.527
pipes+behavior | 73.3851 | 86.2063 | 88.8823 | 89.2002 | 89.1962
hydrosense training results
real-world water usage data
term (i)+(ii)
term (i)
terms (i)-(iv)
*error bars = std error

## Slide 104
Chart: Days of Training Data
| 1 | 3 | 5 | 7 | 10
pipes | 68.9353 | 78.8351 | 80.5773 | 82.352 | 82.9633
pipes+LM | 76.503 | 86.3948 | 87.5797 | 88.3788 | 89.527
pipes+behavior | 73.3851 | 86.2063 | 88.8823 | 89.2002 | 89.1962
hydrosense training results
real-world water usage data
term (i)+(ii)
term (i)
terms (i)-(iv)
*error bars = std error

## Slide 105
Chart: Days of Training Data
| 1.5 | 3.5 | 5.5 | 7.5 | 10.5
pipes+behavior | 73.3851 | 86.2063 | 88.8823 | 89.2002 | 89.1962
hydrosense training results
real-world water usage data
*error bars = std error
terms (i)-(iv)
Notes: here I am graphing percent accuracy, using all terms, versus the number of days of training data. we use days because the language model requires contiguous blocks of data in order to be trained.

## Slide 106
Chart: Days of Training Data
| 1.5 | 3.5 | 5.5 | 7.5 | 10.5
pipes+behavior | 73.3851 | 86.2063 | 88.8823 | 89.2002 | 89.1962
hydrosense training results
real-world water usage data
*error bars = std error
terms (i)-(iv)
Notes: and we will zoom in to see the error bars.
We can see that the 89% accuracy occurs somewhere around 3-5 days of training data. This is interesting to us because it tells us how much data an unsupervised system might need to collect in order to train the current algorithm. So we need the equivalent of about 5 days data.

## Slide 107
pervasive 2011 contributions
longitudinal study of real-world water usage and the resulting dataset
a new probabilistic approach to water usage classification
demonstrate that this new approach can accurately classify real world data
1
2
3

## Slide 108
future work
additional features
segmentation
ease of training
1
2
3

## Slide 111
design:
use:
build:
ubicomp lab
university of washington
sustainability research
university of washington
A Longitudinal Study of Pressure Sensing to Infer Real-World Water Usage Events in the Home
Jon Froehlich, Elliot Saba, Tim Campbell, Les Atlas, James Fogarty and
Shwetak Patel
Eric Larson
eric.cooper.larson@gmail.com

## Slide 122
water tower
thermal
expansion
tank
hose
spigot
utility water meter
pressure regulator
laundry
bathroom 1
hot
water heater
bathroom 2
dishwasher
incoming cold water from supply line
kitchen

## Slide 123
water tower
thermal
expansion
tank
hose
spigot
utility water meter
pressure regulator
laundry
bathroom 1
hot
water heater
bathroom 2
dishwasher
incoming cold water from supply line
kitchen

## Slide 124
water tower
thermal
expansion
tank
hose
spigot
utility water meter
pressure regulator
laundry
bathroom 1
hot
water heater
bathroom 2
dishwasher
incoming cold water from supply line
kitchen

## Slide 125
water tower
thermal
expansion
tank
hose
spigot
utility water meter
pressure regulator
laundry
bathroom 1
hot
water heater
bathroom 2
dishwasher
incoming cold water from supply line
kitchen

## Slide 126
water tower
thermal
expansion
tank
hose
spigot
utility water meter
pressure regulator
laundry
bathroom 1
hot
water heater
bathroom 2
dishwasher
incoming cold water from supply line
kitchen

## Slide 127
three sensing granularities
three levels of granularity

## Slide 129
hydro deployment infrastructure
on-site sensing infrastructure
python web backend
c# and matlab analysis tools

## Slide 130
hydro deployment infrastructure
on-site infrastructure
python web backend
c# and matlab analysis tools
analysis tools
& algorithms

## Slide 131
hot
water heater
water tower
Chart: 
toilet
Chart: 
kitchen sink cold
Chart: 
kitchen sink hot
observation point
valve mechanics: water tank dampening

## Slide 132
water tower
Chart: 
bath
Chart: 
toilet
Chart: 
sink
hot
water heater
valve mechanics: flow rate

## Slide 133
water tower
thermal
expansion
tank
hose
spigot
utility water meter
pressure regulator
laundry
bathroom 1
hot
water heater
bathroom 2
dishwasher
incoming cold water from supply line
kitchen
Chart: 
toilet
Chart: 
kitchen sink cold
Chart: 
kitchen sink hot
Chart: 
Chart: 
bath
dishwasher
upstairs toilet
downstairs toilet
downstairs shower
kitchen sink cold
kitchen sink hot

## Slide 134
water tower
thermal
expansion
tank
hose
spigot
utility water meter
pressure regulator
laundry
bathroom 1
hot
water heater
bathroom 2
dishwasher
incoming cold water from supply line
kitchen
Chart: 
toilet
Chart: 
kitchen sink cold
Chart: 
kitchen sink hot
Chart: 
Chart: 
bath
dishwasher
upstairs toilet
downstairs toilet
downstairs shower
kitchen sink cold
kitchen sink hot

## Slide 135
bath open
dishwasher open
upstairs toilet flush
downstairs toilet flush
downstairs shower open
kitchen sink
cold open
kitchen sink
hot open

## Slide 136
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 

## Slide 137
water tower
hose
spigot
utility water meter
pressure regulator
laundry
bathroom 1
hot
water heater
bathroom 2
dishwasher
incoming cold water from supply line
toilet flushed
toilet
kitchen
thermal
expansion
tank
Notes: The instant a valve is opened or closed (be it a bathroom faucet or a mechanical valve in a dishwasher), a pressure change occurs and a pressure wave is generated in the home plumbing system.

## Slide 138
Chart: 
ground truth labels
for the ubicomp2009 study, we manually provided ground truth labels for the pressure stream during the experiment
kitchen sink

## Slide 139
three levels of granularity
valve level
e.g., upstairs bathroom faucet hot water activated
1
fixture level
e.g., upstairs bathroom faucet activated
2
fixture category level
e.g., faucet activated
3

## Slide 142
in the first study, pressure waves were manually annotated with “ground truth labels” describing:
the fixture used
the water temperature

## Slide 143
magnet
ball switch
reed switch
hot handle movement
ball switch
magnet
reed switch
(hidden)

## Slide 144
accelerometer & ball switch
parent sensor board

## Slide 145
reed switch (hot handle)
reed switch (cold handle)
magnet & ball switch
magnet & ball switch

## Slide 146
reed
switch
magnet
omni-directional ball switch

## Slide 147
omni-directional ball switch
accelerometer

## Slide 148
xbee wireless transmitter
parent sensor board
modified kill-a-watt
washing machine plug
(connects to kill-a-watt outlet)
thermistor cable for drain pipe (in red)

## Slide 149
remember, all this work just to provide labels for hydrosense
Going to use a different slide here that has pressure waves with labels….

## Slide 150
web backend
analysis tools & algorithms
on-site sensing & logging

## Slide 154
Notes: A Hall effect sensor is a transducer that varies its output voltage in response to changes in magnetic field.
A reed switch is an electrical switch operated by an applied magnetic field

## Slide 156
Chart: 
| pipes | pipes+LM | pipes+behavior
 | 70.2017 | 72.4838 | 75.4914
 | 83.4264 | 87.9941 | 89.4856
 | 93.6134 | 95.3645 | 95.9173

## Slide 157
ground truth labels
for the ubicomp2009 study, we manually provided ground truth labels for the pressure stream
kitchen sink
cold
open
cold
close
kitchen sink
hot
open
hot
close
bathroom sink
cold
open
cold
close

## Slide 158
ground truth labels
kitchen sink
cold
open
cold
close
kitchen sink
hot
open
hot
close
bathroom sink
cold
open
cold
close
ball switch
reed switch
hall effect
accelerometer
z
x
y

## Slide 159
automated ground truth labeling method
design goals
hardware capabilities
wireless communication
low-power
water resistant
sensing capabilities
work across fixtures/appliances
detect opens/closes
discriminate hot/cold/mixed

## Slide 160
hydro deployment infrastructure
on-site sensing infrastructure
python web backend
c# and matlab analysis tools

## Slide 161
lots of tape

## Slide 162
lots of tape

## Slide 163
9 reed switches
8 acceler-ometers
14 ball switches
12
pcbs
lots of tape

## Slide 164
flow
control
temperature control
hot flow control
cold flow control
single handle faucet
dual handle faucet
challenge: fixture diversity